## Slide 1: Tube Flocculator Spring 2013
Patience Li
Margaret Fleming

## Slide 2: OUTLINE
Introduction
Experiments
Conclusion
Future Work

## Slide 3: Introduction -- Apparatus

## Slide 5: Experiments: Silicone vs. Tygon
Silicone
Tygon
Goals– Reduce coagulant and clay attachment

## Slide 6: Experiment: Silicone vs. Tygon
Process Controller Method
Set Point | Value
Target influent turbidity | 100 NTU
Raw water flow rate | 5.5 mL/s
Length of tube flocculator (1 unit) | 28 m
PACl base | 1.1
PACl coefficient | 0.9
Max reps | 15

## Slide 7: Experiments: Silicone vs. Tygon
Results
Silicone tube is better!

## Slide 8: Floc Break up Goals
Floc Break up
Orifice size = f (ε)
Positioning of break up points
Capture velocity (constraint)
No. of break up positions
Improve Flocculation Performance

## Slide 9: Experiment: Floc Break up

## Slide 10: Experiment: energy dissipation rate clamp size
Assumptions
1) No vena contracta
2) ID conserved
3) Rectangle + 2 half circles
4) Wall thickness conserved

## Slide 11: Experiment: energy dissipation rate clamp size

## Slide 12: Experiment: energy dissipation rate clamp size

## Slide 13: Experiments: Floc Breakup at Low Coagulant Dose
Results – low PACl dose is not beneficial
Chart: PACl (mg/L)
| 0.0 | 0.9 | 0.99 | 1.089 | 1.198000000000001 | 1.318 | 1.448999999999999 | 1.594 | 1.754 | 1.929 | 2.122 | 2.333999999999999 | 2.568 | 2.825 | 3.107
silicone w/o clamps | 97.375 | 30.11 | 31.828 | 27.565 | 26.785 | 25.195 | 23.629 | 20.472 | 22.089 | 19.74 | 17.893 | 16.919 | 14.575 | 13.405 | 13.25
silicone 2 clamps (4.5 mm) | 98.095 | 59.638 | 50.775 | 41.469 | 35.777 | 35.391 | 31.559 | 32.976 | 29.071 | 28.366 | 25.747 | 25.43 | 23.309 | 21.396 | 21.111
silicone 2 clamps (1cm) | 94.883 | 64.857 | 38.217 | 33.996 | 31.625 | 30.726 | 28.653 | 25.62 | 25.582 | 23.337 | 22.1 | 21.377 | 21.421 | 18.901 | 17.915
silicone 2 clamps 6mm | 94.627 | 47.145 | 38.285 | 39.765 | 34.93 | 31.883 | 30.543 | 28.366 | 26.904 | 22.094 | 21.28 | 21.438 | 18.127 | 17.101 | 16.042

## Slide 14: Experiments: Optimal Coagulant Dose
Ideal situation for floc breakup is what achieves a residual turbidity below 5 NTU Dose = 10 mg/L PACl dose
Chart: PACl Dose (mg/L)
| 0.9 | 1.08 | 1.296 | 1.554999999999999 | 1.866 | 2.239 | 2.687 | 3.225 | 3.87 | 4.643999999999998 | 5.573 | 6.686999999999998 | 8.024000000000001 | 9.629
residual turb NTU | 68.552 | 41.725 | 36.691 | 33.247 | 31.393 | 27.116 | 24.937 | 21.094 | 19.441 | 15.327 | 13.133 | 9.735 | 7.814 | 6.528

## Slide 15: Experiments: Optimal Orifice Size for Floc Break Up Device
PACl dose: 10 mg/L
Orifice sizes (Htube): 0.4 cm, 0.5 cm, 0.6 cm, 1.3 cm (no clamps)
Associated additional energy dissipation rates: >1000 mW/kg, 300 mW/kg, 90 mW/kg, 0 mW/kg

## Slide 16: Optimal Orifice Size for 2 clamp set up
Results: best performance from 5 mm orifice size
Chart: Clamp size
| 1.3 | 0.6 | 0.5 | 0.4
 | 9.047 | 6.934 | 6.381 | 7.936
orifice size without clamps
orifice size with optimal floc break up
(cm)

## Slide 17: Optimal Number of Clamps
PACl dose: 10 mg/L
Orifice size: 5mm
Results:
  Floc Breakup points improve flocculator performance
  Adding more than two clamps at a 5 mm orifice size does not improve flocculator performance
Chart: Number of clamps
| 2.0 | 4.0 | 8.0
 | 6.381 | 7.338 | 6.831
 | 9.047

## Slide 18: Conclusions
Silicone tube provides a more accurate environment for measuring effluent turbidities than tygon
Floc break up is only beneficial at higher coagulant dose.
PACl dose 5 mg/L
PACl dose 10 mg/L

## Slide 19: Conclusions
At a coagulant dose of 10 mg/L, adding clamps improves flocculator performance.
For a two clamp floc break up system, the optimal clamp size is approximately 5 mm.
  When more clamps are added at this orifice size, flocculator performance does not improve.
  It should not be assumed that a 5 mm clamp size remains optimal when clamp number is increased.

## Slide 20: Future Work
Floc Break up:
Optimal orifice size for 2, 4, 8, and 16 clamp system
Optimal break up device positioning
Tapered Flocculation

## Slide 21: Questions