## Slide 1: Demo Plant Team
Susan Chen, Owen Guldner, and Diana Kelterborn

## Slide 2: Introduction
Important educational tool
Used at Cornell for outreach
Used in Honduras to teach operators
Last semester:
  A sedimentation tank and a SRSF were added
  Plant was put on an 80/20 frame

## Slide 3: Objectives
Improve the chemical doser so it works without having to move counterweight
Adjust the filter so all the layers reliably backwash
Improve overall plant layout

## Slide 4: Plant Layout
Constraints
  Sit on a table
  Easily assembled and disassembled
  Professional and neat appearance
  Displayed in order to be easily seen and understood
  Less than six feet tall
  Still many ways to organize the plant…

## Slide 5: Designs

## Slide 6: Current Design

## Slide 7: Stock Tanks and Constant Head Tanks
Clear
Wide-mouth for filling and for stacking
Just large enough
Match each other
Straight sides
Durable

## Slide 8: Paneling
Ensures focus stays on the plant, not on what’s behind the plant

## Slide 9: Sed Tank
Shorter, thinner tubes and smaller fittings
Changed clear well to ½ inch tubing to save room

## Slide 10: Stacked Rapid Sand Filter
Filter didn’t properly backwash
Bottom two layers never fluidized
‘Water gaps’ formed pushing the sand up and out the backwash valve

## Slide 11: Stacked Rapid Sand Filter
We’ve experimented with finer and coarser sand grains.
Finer sand grains formed fewer ‘water gaps’
Tilting the filter column eliminates ‘water gaps’
We will build a taller filter to allow more room for the sand to expand

## Slide 12: Future Work
Build tanks
Make the frame easier to assemble by adding hinges and/or pins
Paint and add the panels
Determine exact flow rates and their corresponding dosages
Finalize the heights of all the processes
Revise the user manual to reflect all of our changes