## Slide 1
Expansion losses

## Slide 2: Head Loss: Minor Losses
greater
Head (or energy) loss due to: outlets, inlets, bends, elbows, valves, pipe size changes
Losses due to expansions are ________ than losses due to contractions
Losses can be minimized by gradual transitions
Losses are expressed in the form where KL is the loss coefficient
When V, KE  thermal

## Slide 3: Head Loss due to Sudden Expansion: Conservation of Energy
zin = zout
Relate Vin and Vout?
in
out
Relate pin and pout?
Mass
Momentum
Where is p measured?___________________________
At centroid of control surface
z
x

## Slide 4: Head Loss due to Sudden Expansion: Conservation of Momentum
Apply in direction of flow
Neglect surface shear
Divide by (Aout g)
Pressure is applied over all of section 1.
Momentum is transferred over area corresponding to upstream pipe diameter.
Vin is velocity upstream.
1
2
A1
A2
x

## Slide 5: Head Loss due to Sudden Expansion
Discharge into a reservoir?_________
Energy
Momentum
Mass
KL=1
2
2
2

## Slide 6: Expansion loss coefficient relative to velocity in pipe
Ain has to be based on the constricted flow area