## Slide 1: Sedimentation Tank Hydraulics
Frances Ciolino
Andrea Fortman
Marlana Hinkley
Marlon Passos

## Slide 2: Experimental Set-Up

## Slide 3: The Set-Up: a Real AguaClara Plant
Lever
Constant Head Tank
Coagulant Stock Tank
Linear Flow Orifice Meter
Dosing Tubes
Flow calibration column

## Slide 4: Experimental Set-Up
Includes the same components
  Raw Water Source
    Aerated tap water
    Addition of clay
    Turbidity measured
  Coagulant stock tank
  Dosing tubes = pump
    Rate adjusted based on raw water turbidity
Flocculator

## Slide 5
Exit Channel
Entrance Channel
Launder
Inlet Manifold
Plate Settlers
Diffusers
Sed Tank Drain
Floc Weir
AguaClara Sedimentation Tank Design
Floc Hopper
Floc Hopper Drain (to remove sludge)
Dump poorly flocculated water channel
Exit Weir that controls water levels all the way back to the next free fall (LFOM!)

## Slide 6: Tank Geometry in a Real Plant

## Slide 7: Experimental Set-Up
Diffusers = Jet reverser
Same bottom geometry
  Weir and floc hopper
  Sludge turbidity measured
Plate settlers = tube settlers
  Effluent turbidity measured
Camera to visually monitor floc blanket

## Slide 8: Goals: What and Why?

## Slide 9: Goals for the semester
Alum dosage
  Do not waste
  coagulant
  Based on Atima numbers
Energy dissipation
  Particle size effect
  Floc blanket effect
Atima Data

## Slide 10: More Goals
Floc hopper depth
  Effect on the sludge
Time till formation
  Relationship between NTU and floc blanket formation
  Help operators
See into floc blanket and hopper
Atima Sedimentation Tank

## Slide 11: Accomplishments

## Slide 12: Research and General Set-Up
Conducted background research
Consolidated the apparatus
Lengthened the flocculator to increase residence time
Altered tank geometry

## Slide 13: Background Research: “Parameters affecting steady-state floc blanket performance”
Gained insight on parameters affecting floc blanket performance
  (1) Energy dissipation, (2) upflow velocity, (3) height and solids concentration in floc blanket, and (4) coagulant dosage
This semester, we plan to test the effects of (1), (3), and (4) on floc blanket formation

## Slide 14: Consolidating the apparatus
Moved to left side of sink
Replaced tubing to decrease head loss through connections
Note: Switched to using PACl
  PACl dosage levels based on those at Atima

## Slide 15: Lengthening the flocculator
Quadrupled the amount of tubing and used a figure-eight pattern rather than the tight coils
  This will increase collisions and more accurately model baffles in AguaClara flocculators
Want to test effect of increased residence time and energy dissipation on blanket formation

## Slide 16: Old Sed. Tank Geometry

## Slide 17: Altered Tank Geometry
New PVC inserts
  More durable, aesthetically pleasing
New Geometry
  Adjustable floc hopper area
Pieces removable with metal rod

## Slide 18: Future Work

## Slide 19: Future Work
Coagulant Dose
  Switch to PAC
  Test three dosages
Pipe Ending Diameters
  Energy Dissipation and Turbidity relationship
  Find the Optimal Point
Chart: Floc Blanket Performance
| 0.5 | 1.5 | 2.5 | 3.5 | 4.5
Energy Dissipation | 5 | 3.5 | 2.5 | 2 | 3.5

## Slide 20: More Future Work
Floc hopper depth
  Heights based on piece sets
  Optical imaging analisys of sludge
  Geometric ratio
Floc blanket formation
  Time and turbidity relationship
Implement contact chamber
Operator management
Notes: Contact chamber and camera capabilities (via Monroe)

## Slide 21: Questions? Comments?