## Slide 1: Foam Filtration
Kristin Chu
Skyler Erickson Melissa Shinbein
Jeffrey Suen
Kadambari Suri

## Slide 2: Last Semester
Notes: JEFF

## Slide 3: This Semester
GOAL: To design and build a fully functioning foam filter.
  Continue brainstorming different compression materials, techniques
  Designing dose controller

## Slide 4: Pulleys

## Slide 5: Structural Support
4 cross drum support pieces
“Box” for balance and stability
Supported by 45 degree extensions
Locking mechanism to hold plunger and disk above the foam

## Slide 6: Plate Design
80/20 support system to distribute force evenly
18” diameter plate with 3/16” holes spaced 1” apart
Water to flow in natural channels of 80/20

## Slide 7: Foam Decompression
Original problem in Honduras
Excess of 1” diameter
Decompresses 14 of 16” almost immediately
DEMONSTRATION

## Slide 8: Side Drain
Problem: Dirty water that sits on top of the compressed foam needs to be removed.
Previous Solution: Siphon  Tested in Honduras.
Improved Solution:
SPIN WELDING
30 PPI
90 PPI
Dirty Water
Notes: Skyler

## Slide 9: Flow Controller
Stock tank: 2.6cm above flow controller
Tubing length: 0.55m
Attaching to drum

## Slide 10: Compression Velocity Test

## Slide 11: Compression Velocity Test
 | Velocity (mm/s) | Influent Turbidity (NTU) | Effluent Turbidity (NTU) | Wash Water Turbidity after Compression (NTU) | Percent Cleaned
Test 1 | 312 | 180 | 0.7 | 978.2 | 104.1%
Test 2 | 128 | 234 | 1.6 | 1029.4 | 80.0%
Test 3 | 39 | 220 | 0.67 | 250 | 3.2%

## Slide 12: Moving Forward
Side exit for effluent water  using SPIN WELDING
Testing the drum (Lab and Honduras)
Packaging system
Answer fundamental questions about foam

## Slide 13: Questions?