## Slide 1: Color Management

## Slide 2: Why Color Management?
Ensures color fidelity to original
Ensures dynamic range of image
In some cases, avoids the need to scan targets with every scan, eliminating the need to crop later on
Avoids the need to adjust the image in post-processing, saving time and human error
Yields significantly higher quality results

## Slide 3: What Is Color Management?
In digital imaging systems, color management is the controlled conversion between the color representations of various devices, such as scanners, digital cameras, monitors, and computer printers.
In scanner profiling, the goal of color management is to achieve neutral values in the RGB channels from white to black, with no clipping of the end points.

## Slide 4: RGB Values Before Profiling

## Slide 5: RGB Values After Profiling

## Slide 6: Color Management Terms*
Calibrate: The process of adjusting a device to known color conditions. Commonly done with devices that change color frequently, such as monitors (phosphors lose brightness over time) and printers (proofers and other digital printing devices can change output when colorant or paper stock is changed).
Characterize- Measurement of device in relation to standard color target. This process creates a profile that describes the unique color conditions found on a particular device.
ICC Device Profile- A file that describes how a particular device (e.g., monitor, scanner, printer, or proofer) reproduces color (i.e., its specific color space). Profiles can be either generic or custom.

## Slide 7
Color Targets
MacBeth - best for manuscript material and silver gelatin prints
Kodak Q13 - ideal when not utilizing color management system
Kodak IT8 - best for contemporary photographs (color glossy paper)
Software
  PictoColor inCamera software for characterizing scanners – Photoshop Plug-in
  Color Eyes Display Pro Device for monitor calibration
Implementing a Color Management System

## Slide 8: Creating A Scanner Profile
1 Scan target in Photoshop | 2 Create the profile | 3 Use the profile
Clean Scanner glass Turn off all automated color adjustment Place chart face down, handling only the edges Crop to edge of target Scan at high-resolution (600 dpi) Save as Targetname_date: macbeth_11_22_09.tif | Open scanned target in Photoshop Clean image, removing any dust, etc Open InCamera in Photoshop : Filter/Picto/InCamera4.5 Adjust as necessary to fit squares in the middle of color patches. Click Ok Save file as Device_MB_Date.icc | Scan material without any auto color adjustment Archive Master file with profile & target scan Assign profile in Photoshop (Edit/Assign Profile) Convert to working space (S-RGB or Adobe) for derivative images (Edit/Convert to Profile

## Slide 9: Sample Workflow for Preservation Master
Turn off automated exposure, automated color, etc
Capture “raw” file
Can either capture with a kodak color chart or archive with profile & macbeth target (or both)
Check white/gray/black values for consistency across channels (if scanning RGB) and tonal range
Archive raw file; make adjustments in PS; archive adjusted file as well.