## Slide 1: CFD Simulation
Travis Stanislaus & Steve Southern
Spring 2010

## Slide 2: Goals
Primary
Obtain an accurate Turbulent Energy Dissipation Map throughout the Flocculator
Issue
CFD has many sources of error that prevent an accurate solution
Secondary
Mitigate the effects of all sources of error
  Discretization Error
    Grid Size
    Solver Order
  Linearization Error
  Wall Treatment
  Turbulence Model
    3D Effects

## Slide 3: Analyzing K - CFD
Extract Cp data at half the flocculator height for all baffle spaces

## Slide 4: Quick Summary
Grid Convergence (Discretization Error)
Iterative Convergence
(Linearization Error)
∆
∆

## Slide 5: Wall Treatment (Verification)
Resolve the viscous sublayer y+ < 5
Avoid the buffer layer 5 < y+ < 30

## Slide 6: Turbulence Model Validation
Chart: -Reynolds Stress/ρ v. Baffle Space #
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
u'u' | 259.8544 | 193.7664 | 710.7556 | 1.7956 | 370.5625 | 0 | 603.6849 | 10.24
v'v' | 155.7504 | 69.2224 | 9.61 | 27.04 | 5.76 | 0 | 0 | 18.8356
w'w' | 1838.6944 | 4624 | 2498.0004 | 2980.0681 | 2601 | 0 | 3452.7376 | 2396.1025
u'v' | -201.1776 | 115.8144 | 82.646 | 6.968 | -46.2 | 0 | 0 | 13.888
u'w' | -691.2256 | 946.56 | 1332.4668 | 73.1506 | 981.75 | 0 | 1443.7332 | 156.64
v'w' | 535.1424 | 565.76 | 154.938 | 283.868 | -122.4 | 0 | 0 | 212.443

## Slide 7: Analyzing K - Experiment

## Slide 8: Turbulence Model Validation
Chart: K v. Baffle #
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
k-ε standard | 4.6214 | 4.3666 | 3.984 | 4.0245 | 4.0282 | 4.0278 | 4.028 | 4.0241
k-ε realizable | 5.3756 | 6.4496 | 4.2066 | 4.2823 | 4.3655 | 4.3679 | 4.3681 | 4.3618
k-ω standard | 6.2694 | 9.2075 | 9.5283 | 9.4538 | 9.29 | 9.2003 | 9.1777 | 9.1449
RSM Linear | 5.7578 | 5.4224 | 2.6558 | 3.2875 | 3.3192 | 3.2848 | 3.286 | 3.2777
RSM SSG | 5.7899 | 7.2877 | 4.4373 | 3.5742 | 3.9821 | 3.9814 | 3.9625 | 3.9397
Experiment | 2.16 | 1.89 | 1.89 | 1.56 | 1.56 | 1.89 | 1.89 | 1.73

## Slide 9: Discretization Order
Chart: K v. Baffle #
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
k-ε standard (1st) | 4.6214 | 4.3666 | 3.984 | 4.0245 | 4.0282 | 4.0278 | 4.028 | 4.0241
k-ε standard (2nd) | 4.4419 | 3.6697 | 3.7553 | 3.7849 | 3.7836 | 3.7835 | 3.7836 | 3.7778
k-ε realizable (1st) | 5.3756 | 6.4496 | 4.2066 | 4.2823 | 4.3655 | 4.3679 | 4.3681 | 4.3618
k-ε realizable (2nd) | 6.0763 | 8.3658 | 3.9985 | 4.0634 | 4.3132 | 4.3104 | 4.3088 | 4.2996
RSM Linear (1st) | 5.7578 | 5.4224 | 2.6558 | 3.2875 | 3.3192 | 3.2848 | 3.286 | 3.2777
RSM Linear (2nd) no conv. | 6.2341 | 5.2538 | 2.0004 | 2.9691 | 2.9022 | 2.8718 | 2.8825 | 2.8653
Experiment | 2.16 | 1.89 | 1.89 | 1.56 | 1.56 | 1.89 | 1.89 | 1.73

## Slide 10: Wall Treatment (Validation)
Enhanced Wall Treatment (y+ < 5)
Standard Wall Functions (y+ > 30)

## Slide 11: Wall Treatment (Validation)
Chart: K v. Baffle #
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
k-ε standard (2nd) normal | 4.4419 | 3.6697 | 3.7553 | 3.7849 | 3.7836 | 3.7835 | 3.7836 | 3.7778
k-ε standard (2nd) refined | 4.4355 | 3.676 | 3.7606 | 3.7883 | 3.7865 | 3.7867 | 3.7864 | 3.7808
k-ε standard (2nd) less ref. | 4.3328 | 3.4431 | 3.4661 | 3.4966 | 3.4965 | 3.4973 | 3.4981 | 3.4952
Experiment | 2.16 | 1.89 | 1.89 | 1.56 | 1.56 | 1.89 | 1.89 | 1.73

## Slide 12: 3D Case

## Slide 13: 3D Results
Chart: K v. Baffle #
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
k-ε standard (2D) | 4.6214 | 4.3666 | 3.984 | 4.0245 | 4.0282 | 4.0278 | 4.028 | 4.0241
k-ε standard (3D) | 4.5081 | 4.6288 | 4.0871 | 4.0962 | 4.1043 | 4.105 | 4.1051 | 4.0992

## Slide 14: Verification/Validation Summary
Discretization Error (Grid Size) < 1%
Linearization Error (Iteration) << 1%
Wall Treatment y+ < 5 or y+ > 30
  Not necessary that y+ << 5
Anisotropic Reynolds stresses call into question eddy-viscosity models (k-ε, k-ω)
Results show eddy-viscosity models over predict experimental K by a factor of 2
RSM over predicts by a factor of 1.5
No significant difference between:
  1st and 2nd order discretization
  Standard and enhanced wall functions
  2D and 3D

## Slide 15: Orifice (Validation Study)
Compare the Discharge Coefficient, Cd, calculated in Fluent with measured values of Cd.
Discharge Coefficient of Orifice |  | 
Re | Cd calculated from Fluent | Cd from “Fluid Mechanics” by Frank White
104 | 0.6285 | 0.633
105 | 0.6087 | 0.611
106 | 0.606 | 0.6

## Slide 16: Orifice (Validation Study)
Compare plots of dimensionless wall-static pressure and centerline velocity of orifice simulation in Fluent with experimental measurements.

## Slide 17
Chart: Orifice wall-static pressure
| -5.0149999999999908 | -3 | -2.0299999999999998 | -1.9000000000000001 | -1.2 | -0.8 | -0.5 | -0.2 | 0 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 10 | 11 | 12
measured data | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | -0.37 | -0.37 | -0.4 | -0.39 | -0.37 | -0.33 | -0.28 | -0.24 | -0.18 | -0.12 | -0.1 | -0.07 | -0.05 | -0.04 | -0.03 | -0.03 | -0.02 | -0.01 | -0.01 | 0 | 0 | 0

## Slide 18
Chart: Centerline axial velocity
| -7 | -4 | -3.5 | -3 | -2.5 | -1 | -0.9 | -0.30000000000000032 | -0.2 | 0.2 | 0.5 | 0.75000000000000122 | 1.5 | 2.25 | 3 | 3.25 | 3.75 | 4 | 4.5 | 5 | 5.5 | 6.5 | 7.25 | 7.5 | 8 | 8.25 | 8.5 | 9 | 9.5 | 10 | 11 | 12 | 13 | 15 | 17
measured data | 0.14 | 0.15 | 0.15 | 0.15 | 0.15 | 0.19 | 0.22 | 0.5 | 0.55 | 0.8 | 0.9 | 0.97 | 1 | 1 | 0.99 | 0.96 | 0.92 | 0.85 | 0.77 | 0.73 | 0.62 | 0.46 | 0.35 | 0.3 | 0.27 | 0.25 | 0.22 | 0.16 | 0.14 | 0.18 | 0.15 | 0.14 | 0.14 | 0.14 | 0.14

## Slide 19: Final Words on the Orifice
Recirculation zone length from orifice
Experiment: 0.13161 m
k-ε realizable: 0.2 m
RSM: 0.185 m
K from measurements and Fluent
Kmeasurement= 31.04
Kfluent= 27.76

## Slide 20: U-Duct (Benchmark)
Chart: Cp v. Position

## Slide 21: A Problem in the other Validation Studies
K obtained from the energy is not time averaged therefore it does not include the turbulent kinetic energy.

## Slide 22: Future Challenges
Understand K for both CFD and experiment
Understand the differences between turbulence models
Perform a large eddy simulation (LES)
Create a rapid mix model

## Slide 23: Questions?