## Slide 1: Tube Floc Experiments
Final presentation Spring 2010
Tami Chung
Sophie Bernat
Alex O’Connell
Dali Sun

## Slide 2: Table of Contents
Introduction
Presentation of the apparatus
Results of our experiments
Problem with the apparatus
Test suspension
Conclusion

## Slide 3: Introduction
Goal:
  Understand flocculation in AguaClara plants
  Study the parameters that influence the results of flocculation.
    Residual turbidity
    Settling velocities

## Slide 4
Flocculation
Coagulant agent : Alum [Al2(SO4)3*14.3H2O]
Charge neutralization or sweep flocculation

## Slide 5: Flocculation
Important parameter
  Terminal velocity
  Collision Potential

## Slide 6
Raw Water Bucket
Clay Stock Bucket
Clay Stock Control Valve
Influent Turbidimeter
Pump to Turbidimeter

## Slide 7
Alum Stock Bucket
Alum Pump
Raw Water Pump
Influent Turbidimeter

## Slide 8
Tube Flocculator
  Can be run at three different lengths depending on the number of tubes used (28 m, 56 mm, and 84 m)

## Slide 9
Ball Valve
Effluent Turbidimeter
Settling Column

## Slide 10: Obtaining the Residual Turbidity Graph…
Plot of Raw data: Turbidity vs. Sedimentation Velocity throughout experiment
Focusing on Residual Turbidity: Residual Turbidity vs. Sedimentation Velocity

## Slide 11
Chart: Alum Dose (mg/L)
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0
5 NTU, 28 m | 4.718 | 1.742 | 1.006 | 0.761 | 0.653 | 0.712 | 0.627 | 0.633 | 0.655
5 NTU, 84 m | 3.967 | 3.405 | 0.452 | 3.114 | 2.717 | 1.3 | 0.724 | 0.663 | 0.876 | 0.723
5 NTU Results
Gθ values of 22951 and 68853, respectively

## Slide 12
Chart: Alum Dose (mg/L)
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
100 NTU, 28 m | 20.129 | 5.001 | 2.411 | 1.562 | 1.031 | 0.753 | 1.027 | 0.849 | 0.983 | 1.133
100 NTU, 56 m | 68.948 | 71.828 | 70.147 | 68.867 | 30.749 | 7.367 | 2.469 | 1.169 | 0.866 | 0.784
100 NTU, 84 m | 55.283 | 24.677 | 27.322 | 17.561 | 6.361 | 2.395 | 1.578 | 1.263 | 1.238 | 1.365
100 NTU Results
Gθ values of 22951, 45902, and 68853 respectively

## Slide 13
Chart: Alum dose (mg/L)
| 0.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
500 NTU, 28 m | 124.745 | 119.753 | 96.038 | 5.529 | 4.011 | 3 | 3.817 | 2.372 | 2.143 | 2.056 | 1.895
500 NTU, 56 m | 124.219 | 107.545 | 14.032 | 6.276 | 5.112 | 3.849 | 3.079 | 3.219 | 3.043 | 2.929 | 2.889
500 NTU, 28 m replicate | 71.508 | 54.105 | 8.646 | 5.355 | 5.225 | 5.676 | 4.528 | 3.306 | 2.925 | 2.517 | 2.349
500 NTU Results
Gθ values of 22951 and 45902, respectively

## Slide 14
Reproducibility of Results
Chart: Alum dose (mg/L)
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0
5 NTU, 28 m | 4.867 | 1.487 | 2.034 | 0.825 | 0.815 | 0.789 | 0.812 | 0.757
5 NTU, 28 m replicate | 4.718 | 1.742 | 1.006 | 0.761 | 0.653 | 0.712 | 0.627 | 0.633
Chart: Alum dose (mg/L)
| 0.0 | 1.5 | 2.25 | 3.374999999999999 | 5.062999999999996 | 7.593999999999999 | 11.391 | 17.08599999999998 | 25.629
5 NTU, 84 m | 3.967 | 3.405 | 0.452 | 3.114 | 2.717 | 1.3 | 0.724 | 0.663 | 0.876 | 0.723
5 NTU, 84 m replicate | 2.764 | 2.513 | 2.272 | 2.035 | 2.016 | 1.437 | 0.846 | 0.635
Chart: Alum Dose (mg/L)
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
100 NTU, 56 m | 75.936 | 64.486 | 1.773 | 0.786 | 0.64 | 0.691 | 0.664 | 0.714 | 0.995 | 0.878
100 NTU, 56 m low alum dosages | 68.948 | 71.828 | 70.147 | 68.867 | 30.749 | 7.367 | 2.469 | 1.169 | 0.866 | 0.784 | 0.661
Chart: Alum Dose (mg/L)
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
100 NTU, 84 m | 3.297 | 1.828 | 1.108 | 1.863 | 1.53 | 1.349 | 1.543 | 1.774 | 1.412 | 1.724
100 NTU, 84 m replicate | 2.306 | 1.248 | 1.643 | 1.661 | 1.349 | 1.547 | 1.434 | 1.569 | 1.338 | 1.932
100 NTU, 84 m low alum dosages | 55.283 | 24.677 | 27.322 | 17.561 | 6.361 | 2.395 | 1.578 | 1.263 | 1.238 | 1.365 | 1.047
5 NTU
100 NTU

## Slide 15: Results : Mean sedimentation velocities
Mean sedimentation velocities calculated when fitting the data to a gamma distribution

## Slide 16: Results : Mean sedimentation velocities
No sedimentation velocities 5 NTU influent water

## Slide 17: Results : Mean sedimentation velocities
Alum Dose : Different depending on influent turbidity
  100 NTU

## Slide 18: Results : Mean sedimentation velocities
500 NTU

## Slide 19: Results : Mean sedimentation velocities
Effect of flocculator length

## Slide 20: Results : Mean sedimentation velocities
Influence of the influent turbidity

## Slide 21: Influence of Alum Line clogs on Result
Problem
  Alum mixed in Distilled water instead of tap water
  Solid coagulant formed when alum mixed with raw water
Effecting Data
  Solid precipitation can build up over time restricting flow

## Slide 22: Solid precipitation blocked alum flow
Chart: Alum Dose (mg/L)
| 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
100 NTU, 56 m | 75.936 | 64.486 | 1.773 | 0.786 | 0.64 | 0.691 | 0.664 | 0.714 | 0.995 | 0.878
100 NTU, 56 m low alum dosages | 68.948 | 71.828 | 70.147 | 68.867 | 30.749 | 7.367 | 2.469 | 1.169 | 0.866 | 0.784 | 0.661

## Slide 23: Test Suspension
Goal: Verify the validity of results given by FReTA
Plan: To input known mixture of distilled water and particle beads and compare theoretical sedimentation velocity values to those of the empirical.

## Slide 24: Current Progress and Problems Encountered
New simplified experimental apparatus set up completed
Problems with the latex particle beads
  Translucent
  Tendency to clump together

## Slide 25: Conclusion: What We Know So Far...
Variation of Alum Dose/Flocculator Length
General Trend:
  Residual Turbidity:
    Alum dose and flocculator length
  Mean Sedimentation Velocity
    Influent turbidity and alum dose
    Flocculator length

## Slide 26: Future Challenges
Continue and complete the analysis of variation of alum dosage and flocculator length
Complete verification experiment of FReTA
Study the effects of PH on flocculation

## Slide 27: Thank You
Monroe Weber-Shirk
Matthew Hurst
Julie Pierce

## Slide 28: QUESTIONS ?