## Slide 1: Tube Floc - Teach in
Tami Chung
Sophie Bernat
Alex O’Connel
Dali Sun

## Slide 2: What we will talk about…
Theory on flocculation
Experimental set up
Current research

## Slide 4: Flocculation
Electrostatic
What causes the turbidity of the water ?
  Colloidal particles

## Slide 5
Flocculation
Decrease magnitude of energy barrier
  change the charge of the particles
  introduce positively charged particles
Coagulant agent : Alum [Al2(SO4)3*14.3H2O]
Charge neutralization or sweep flocculation

## Slide 6: Flocculation
Important parameter
  Terminal velocity

## Slide 7: Flocculation
Collision potential

## Slide 8
FReTA Experimental Setup: The Equipment We Use to Analyze Flocculation

## Slide 9
Raw Water Bucket
Clay Stock Bucket
Clay Stock Control Valve
Influent Turbidimeter
Pump to Turbidimeter

## Slide 10
Alum Stock Bucket
Alum Pump
Raw Water Pump
Influent Turbidimeter

## Slide 11
Tube Flocculator
  Can be run at three different lengths depending on the number of tubes used (2796 cm, 5592 cm, and 8388 cm)

## Slide 12
Ball Valve
Effluent Turbidimeter
Settling Column

## Slide 13
FReTA Verification Test
Use two different particle sizes with known
settling velocities at a known turbidity
Particles will be in a closed recirculation system
Compare FReTA’s measured settling velocity to the actual settling velocity

## Slide 14: Goals and Challenges
Goal: To study the effects of different flocculator lengths and alum doses on effluent turbidity
How:
  Varied alum dosage at constant increments
  Applied the set alum dosages to three different flocculator lengths.

## Slide 15: Data Analysis
Process Controller
  A Mathcad program that gives graphical overviews of processed data.
What to look at:
  Residual Turbidity Graph

## Slide 16: Obtaining the Residual Turbidity Graph…
Plot of Raw data: Turbidity vs. Sedimentation Velocity throughout experiment
Focusing on Residual Turbidity: Residual Turbidity vs. Sedimentation Velocity

## Slide 17: Residual Turbidity vs. Sedimentation Velocity
Alum Dose | Residual Turbidity
20 | 2.663
25 | 1.755
30 | 1.81
35 | 1.497
40 | 1.437
45 | 1.413
50 | 1.325
55 | 0.984
Notes: 100 NTU experiement @ 1st flocculator length.

## Slide 18: Organization and Analysis
Results from Process Controller plotted on Excel
Reiterate experiment for verification

## Slide 19: Future Plans
Complete testing other alum dosages and flocculator lengths.
Further analyze and study current experiments.
...Next Experiment planned?
  Study the effect of PH on flocculation