## Slide 1: Floc Hopper Probe Fabrication Subteam
Garret Janich
Steve Love

## Slide 2: Initial Dilemma
Problem: Limited visibility into floc hopper at the end of sedimentation tanks. This is important to keep the sludge level regulated and minimize cleaning requirements.
Solution: Model a probe to peer through the 2” openings along the settled water channel. The waterproof tube is ideal for telescopic view as well as with a snake camera.

## Slide 3: First Sketches
Pipe setup and camera reflector options

## Slide 4: Sketches

## Slide 5: Prototype 1

## Slide 6: Camera Solution
Layers:
  Camera
  Duct tape collar
  Small flexible pipe

## Slide 7: Challenges & Development
Development:
Borescopic camera fixated to a smaller internal tube for weight to concentrate direction.
Slanted removeable plate promotes sludge runoff.
Horizontal lines drawn on plate to determine depth.
Challenges:
Distance between glass lens and plate should be at a ½”.
GLARE! The borescopic snake camera’s built-in LED causes disruptive reflection in glass lens.
Built up sludge may interfere with light - especially when located externally.

## Slide 8: Current Design

## Slide 9: Next Steps in Design
Opaque plate allows for light visibility in the dark tank environment.
Choose optimal light type and fixture setup to illuminate plate.
Waterproof bulb options:
  LED “Candle”
    Pros: Remote control
    Cons: Single source of light
  Mini LED Balloon Lights
    Pros: Diverse points of light
    Cons: Undecided method of securing attachment

## Slide 10: Next Steps in Imaging
Program camera to correspond images and image data to laptop.
Develop for use with a computer/smartphone interface.
Imaging methods should be expanded upon.
Explore probe head design to optimize even light transmittance for imaging quality.

## Slide 11: Shoutouts & Thanks
Ethan for sublime subteam leadership and consultancy.
Casey for deciphering part descriptions and ordering from many vague emails.
Monroe for an awesome experience and a great highlight to my resume.
All the fabrication subteam members for valuable suggestions and insights.
HAPPY SUMMER EVERYONE!!!
Sharkbait Ooh-HaHa

## Slide 12: Questions
Questions?
Feedback:
  How can we improve our design?
  How else can the device be used?
  How does our research overlap?