## Slide 1: Fabrication
Juan Saavedra
Guo Jie Chin

## Slide 2: Introduction
Goal: to design and implement procedures to make the building process more efficient
Problems we approached
  Decrease time required to drill holes
  Improve battery life of cordless drill
  Design method to easily align plate settlers

## Slide 3: Car Battery
Problem: Cordless drill used on site runs out of power frequently
Utilize a portable power source such as a car battery to drive it
  Direct power was not feasible due to complicated circuitry of battery

## Slide 5: Car Battery
DC Battery Charger produced by Milwaukee

## Slide 6: Car Battery
Promising results: Charge time of 42 minutes in our test
Advantages
  Safe, reliable
  Efficient, quick charge
Disadvantages
  Requires multiple swappable batteries

## Slide 7: Car Battery
Future goals
  Research alternative sources of power
    Solar
    Mechanical Dynamo (e.g Bicycle)

## Slide 8: Hole Saw
Problem: hole saw plugs are difficult to remove
                Idea: use a different type of drill bit or saw

## Slide 9: Hole Saw
Drill bits
Forstner Bit
Step Bit
Plastic Bit
Spade Bit

## Slide 10: Hole Saw
Lenox speed-slot saw
  Uses a lever system to facilitate plug removal
  Worked much faster and more efficient in our tests

## Slide 11: Hole Saw
Future goals
  Develop a specialized tool to pry out plug
  Design a tool to act as an elevated pivot for any general hole saw

## Slide 12: Plate Settlers
Current issue
  Difficult to align and drill holes effectively, since plates are to be placed at an angle

## Slide 13: Plate Settlers
Our idea was to construct a jig that would allow workers to easily align plates
Knowing the angle of inclination, a geometric analysis gives us the necessary spacing

## Slide 14: Plate Settlers
Initial jig: 1.15cm height difference results in 2cm plate separations

## Slide 15: Plate Settlers
Issues
  Sacrifice accuracy for efficiency
    Hard to align since jig sheets were thin
    Hard to visually confirm if they were well aligned
Try building with a different material

## Slide 16: Plate Settlers
Jig 2.0: Utilizing a thicker material
  Flatness does not matter – was actually easier to align
  Thicker material ensures accuracy

## Slide 18: Plate Settlers
Jig 3.0
  Same material, but built using measurements of current designs being built
  Constructed slightly wider, and extended to fit up to 10 plates at a time
  Built with a 90 degree corner to nudge plates in

## Slide 19: Plate Settlers

## Slide 20: Plate Settlers
Future goals
  Find easier ways to measure initial holes
  Create different or multiple jigs to work for different plate spacings

## Slide 21: Questions?