## Slide 1: Fabrication
Juan Saavedra
Guo Jie Chin

## Slide 2: Objectives
Extend battery life of cordless drill used on site
Improve hole saw cutting efficiency
Implement an efficient method to construct plate settler modules

## Slide 3: Drill Battery
Current situation
  New multipurpose drill acquired
  Limited usage
  Previous year’s team recommended utilizing the power of a car battery
Initial ideas
  Wire drill directly to a car battery
  Utilize DC power to charge the battery

## Slide 4: Drill Battery
Internal circuitry of the battery pack proved to be quite complex
We concluded that a direct connection is not a feasible route

## Slide 5: Drill Battery
Charging Battery with DC power
  The drill manufacturer produces a cigarette lighter DC battery charger
  Equipment arrived this week, and we will begin testing charge times and usability

## Slide 6: Drill Battery
Benefits
  Versatile
  Causes no permanent damage or
  Safe
Drawbacks
  May result in down time if there are not enough batteries to cycle through
  Many connectors/adapters

## Slide 7: Hole Saw
Current issue
  Stuck plugs in the saw are difficult to remove

## Slide 8: Hole Saw
Use a specialized tool
  One end is a step to use as a lever, the other end is to pry out the plug

## Slide 9: Hole Saw
Tool was hard to stabilize and adjust
The prying end worked, but material was easily bent and rendered unusable
Not a viable method

## Slide 10: Hole Saw
Lenox Speed-Slot Hole Saw
  Designed to facilitate removal of hole plugs
  Uses a step system much like our tool to provide multiple lever points

## Slide 11: Hole Saw

## Slide 12: Hole Saw
Advantages
  Worked effectively and more efficiently
  Not much more expensive ($10-15 more)
Disadvantages
  Very specialized & hard to find

## Slide 13: Plate Settlers
Current issue
  Difficult to align and drill holes efficiently
  Previous year’s team proposed using a jig to align and stack plates
Our idea is to manufacture a jig that ensures a 2cm spacing between plates
Need to know height difference

## Slide 14: Plate Settlers
Since angle of inclination is 60 degrees, a height difference of 1.15cm gives 2cm separation between plates

## Slide 15: Plate Settlers
Built using seven 1.15cm long strips of successively layered lamina

## Slide 16: Plate Settlers
Looking forward
  Evaluate the efficiency of the jig by constructing an entire plate module
  Extend the jig so it is able to handle more plates at a time for larger modules