## Slide 1: Stock Tank Mixing
Alexandra Cheng
Apoorv Gupta

## Slide 2: Semester Goals
Stock Tank Mixing Pump
  Design high efficiency device to uniformly mix stock solutions
  Perform small-scale testing and make design adjustments
  Provide design schematic for full-size pump
Hydrometer
  Chlorine density measurement

## Slide 3: Fall 2013 Pump Design
Centrifugal pump
Raise dense solution to higher elevation using pressure gradient

## Slide 4: Bucket Mixer Design
Bucket with 16 0.156” diameter holes
Base projected area approximately 33% of tank base area
Designed to be 80% filled with dense solution at end of cycle
Raise bucket from bottom to top of tank in 5s, wait for bucket to empty and plunge back down

## Slide 5: Plate Mixer Design
1” PVC plate, 33% of tank base area
Create jets and turbulence to encourage mixing
Lift mixer within the height of the dense solution and plunge up and down

## Slide 6: Result Comparison: Bucket vs. Plate

## Slide 7: Base-Level Water Injection
Inject water into the bottom of the stock tank containing dense solution
HL = 2.1 cm due to injection, 31.9 cm due to water transport

## Slide 8: Water Injection Results

## Slide 9: Water Injection Full-Scale Schematic
Head Loss due to injection set at 50 cm
Total Head Loss 1.332 m
Required orifice size = 2.143 mm diameter
Best procedure:
  30% of water + stirred in coagulant
  Remaining 70% of water injected at base level
  Complete mixing using the plate mixer

## Slide 10: Future Work
Finalize design schematics for full-scale water injection system and plate mixer
Continue researching devices to be used for chlorine density measurement and test effectiveness and reliability

## Slide 11: Questions