## Slide 1: Stock Tank Mixing Team
Spring 2011
Midterm Teach-in
Jae Lim, Boyang Mao, Chris Inferrera

## Slide 2: Introduction
Brief Look at Current Mixing System
  Tanks are Rotoplas (200 gallons) or 55 gallon drums

## Slide 3: Introduction
  Tanks hold coagulant solution used for flocculation
  Operator physically mixes coagulant and water in tank

## Slide 4: Introduction
Current Mixing System Problems
  Not feasible for large plants
  Inefficient
  Horizontal Mixing
  No way to tell when solution is fully homogenized

## Slide 5: Team Goals
Design a mixing system that will:
  Reduce operator effort
  Easily achieve high concentrations
  Be scalable to larger plants
Create operating guidelines
Find a reliable and cost effective supplier for granular PACl

## Slide 6: Aluminum Sulfate (alum)
Alum was our initial area of focus
It is currently used at all plants except for Marcala, Cuatro Comunidades (PACl)
Initial mixing designs were made for alum

## Slide 7: Aluminum Sulfate (alum)
Properties
  Denser than water
  Does not readily dissolve

## Slide 8: Aluminum Sulfate (alum)
  Forms “cake” substance when portions are hydrated
  Viscous at high concentrations
Notes: ‘cake’ much harder to dissolve

## Slide 9: Finding the Viscosity of Alum
Existing Data
Viscometers
Decided that for the range of concentrations we would be working with, most likely not an issue.
Gurevich, et al. (2003)

## Slide 10: Inspiration for 1st Design
Source - Schulz and Okun, Surface Water Treatment for Communities in Developing Countries

## Slide 11: 1st Mixing Design
“Double Bucket”
Keeps coagulant fully saturated at all times
Relies on head pressure to mix coagulant
Filter ensures full mixing
Minimal operator work needed

## Slide 12: Problems with 1st Design
Available head pressure not sufficient to dissolve alum
Alum would clog pores

## Slide 13: 2nd Design “Upflow”
Goal – To create a design that would incorporate a flow of water upward into mixing container
Upward flow would work against gravity to create turbulence
Experimented to determine what concentrations would be achievable

## Slide 14: “Upflow” Testing

## Slide 15: Results
Filter at top of set-up source of problems
Unable to measure concentration from first tube

## Slide 16: Transition to PACl
Less denser than water !
Mixes more readily than alum

## Slide 17: Transition to PACl
AguaClara plants are switching to PACl
  More cost efficient than alum
Conversation with Antonio Elvir to learn more about PACl

## Slide 18: Information from Antonio Elvir
Use a maximum of 120 g/L at 4 Comunidades
Use a maximum of 70 g/L at Marcala
Rapid dissolve time (5 min)
At Marcala a mixing device with blades is used
At 4 Comunidades, a tube is used for stirring

## Slide 19: Future Plans
Step 1: Research properties of PACl and determine the highest concentration that can be practically made in AguaClara plants.
  Solubility limit, viscosity as a function of concentration, etc.
Step 2: Determine (in a given concentration level) if the solution can be homogenized throughout the tank to an acceptable degree.
  Concentration levels throughout the tank.

## Slide 20: Future Plans
Step 3: Determine the acceptable range of PACl concentrations in plants.
Step 4: Set up operating guidelines.
  Currently, operators can only inspect visually to judge if the solution is saturated.
  Calculate the energy input (i.e. number of stirs) necessary.

## Slide 21: Future Plans
Step 5: Determine if a new mixing design is needed.
  Will the solution be more homogenized with a new mixing system?
    Currently, only horizontal mixing for 55 gallon drums.
  Current mixing system in place is acceptable, but not viable for large plants.
  Perhaps adding PACl before water will help mix the solution (extra energy input).

## Slide 22: PACl Supply
31% Al2O3 PACl
Henan Billions Chemicals (North American Division)
  The PACl in the Cornell labs is a sample provided by this company
  We have to import it from China (expensive)

## Slide 23: Potential U.S. Suppliers
Grasim Chemicals
Tulstar Products, Inc.
Kaixin Chemicals Co., Ltd.
Holland Company
More than 90% of granular PACl suppliers are from China.

## Slide 24: Finding Granular PACl…
U.S. Chemical companies usually provide liquid PACl.
If we cannot find a reliable supplier in the U.S. may need to find the most cost effective international source.

## Slide 25: Conclusion
AguaClara plants leaning towards using PACl in the future
New focus for mixing system research is on PACl.
Try to find PACl supplier as soon as possible for future use.

## Slide 26: Questions?