## Slide 1: Stacked Rapid Sand Filtration-Full Scale
Michelle Wang
Steph Lohberg
Chris Holmes

## Slide 2: Stacked Rapid Sand Filter
Inlet Box
Outlet Box
Backwash Cycle
Filtration Cycle
Air Trap
Sand Bed
Valve
Siphon
Pipe

## Slide 3: Model Dimensions

## Slide 4: SRSF in Tamara-Issues Pipe Connections

## Slide 5: SRSF in Tamara-Issues Pipe Connections

## Slide 6: SRSF in Tamara-Issues Pipe Connections

## Slide 7: Molding Process
Boiling Water
  Did not work
    Water was at a full boil
    Added salt
    Considered other additives
Heat Gun
  Works very efficiently
  Less than a minute
Types of Molds
  Tapered Mold
    Too much of a Taper
    Loose when connected to pipe
  Straight Mold
  Curved Cylindrical Mold

## Slide 8: Different Molds
Mold for the 6’’ pipe

## Slide 9: Different Molds
Mold for the 2’’ pipe

## Slide 10: Different Molds-Diagrams
Straight Mold Curved Mold

## Slide 11: Molding Video Process
http://www.youtube.com/watch?v=Bl-fKro20Ec

## Slide 12: Assembly Process
Pipes are directional
Construct outside of box
Still able to exchange individual pipes when necessary
Also, no sealants or epoxies

## Slide 13: Weaknesses
Pipes connection gaps
  Fixed by enlarging the mold
Flexing
  Fixed by using cables

## Slide 14: Cables
Different design strategies
  Lateral design doesn’t give enough horizontal flex support
  Creating an X gives stability in all directions
  Adding a single lateral cable gives vertical stability

## Slide 15: Zip Ties and Turnbuckles
Zip ties vs. Turnbuckles
  Initial idea used turnbuckles which could get tighter
  Then zip ties were cheaper and created a default strength

## Slide 16: Assembly Problems
Caps and Couplings (Fernco vs. PVC)
Consistency with creating holes
Stacking

## Slide 17: Assembly Video Process
http://www.youtube.com/watch?v=oTHYG9axKW

## Slide 18: Stacking Layers
Alternative method - no T connections
Zip-ties as a viable option
Functions in backwash
Easy to manufacture
Easy removal

## Slide 19: Future Work
Test stacking methods
Cable fastening
Low-Flow plant