## Slide 1: Venturi and Low Flow Flocculator
Ryan Anthony, Elyssa Dixon and Zac Edwards

## Slide 2: Flocculation Overview
Turn smaller particles into larger particles
  Large particles are removed more easily in sedimentation and filtration
  Needs: “Sticky particles” and Collisions

## Slide 3: Flocculation Overview
Channels
Upper Baffles
Ports between channels
Entrance
Lower Baffles
Exit

## Slide 4: Flocculation Overview
H = Water depth
L = Length of the flocculator channel
S = Space between baffles (and between the bottom of the tank and bottom of the upper baffles)
H
L
S
S
S
Upper baffle
Lower baffle
Minimum water level
Port from previous channel
Exit to the sedimentation tank entrance channel

## Slide 5: Collision Potential
Ability to Provide Collisions Between Flocs
Characteristic of the Flocculator
  Increase Size of Floc (to a point)
  Make it Easier for Flocs to Settle Out In Sed Tank
  Lower Residual Turbidity in Effluent

## Slide 6: Question: Why Do We Need a Low Flow Flocculator?
Answer: To supply clean water to small, thirsty Honduran towns!
Another Question: But Why Not Use the current design tool to fabricate one?
Another Answer: Design is Inefficient and Costly

## Slide 7: What Makes the Design So Unattractive?
Too Many Constraints! Certain dimensions of Flocculator
Need Proper Mixing
Lots of Baffles
Inadequate Space
Non-Uniform Energy Dissipation
Energy Dissipation:
∙Rate at which mechanical energy is lost to thermal energy
∙Measure of Turbulence
∙eMax determines max floc size!
Notes: Constraints: Length of flocculator = length of sed tank
Spacing between baffles >= human hip for cleaning purposes

## Slide 8: Visuals
Baffle Spacing vs. eMax
Baffle Spacing vs. Flow rate
Vs.

## Slide 9: Potential Designs
Start with simplest design
Baffle
Pipe Wall
Side View
String
Notes: Using a pipe to model – not limited to constraints like the current plant designs for open flow.
Why is a pipe not so great?
Can’t see inside

## Slide 10: Potential Designs
Pipe
Baffle
Top View

## Slide 11: Potential Designs

## Slide 12: What Have We Done?
Notes: With less constraints we can shoot for optimal efficiency
Modeled plates on a string geometry (still debugging) – similar to current design
Plan to: Model our other 2 designs, evaluate what scenarios designs are applicable for (direct into filter, flow rate, etc), build and test, add pipe flocculator to AguaCLara arsenal

## Slide 13: The End