## Slide 1: Venturi and Low Flow Flocculator
Ryan Anthony, Elyssa Dixon and Zac Edwards

## Slide 2: Flocculation Overview
Turn smaller particles into larger particles
  Large particles are removed more easily in sedimentation and filtration
  Needs: “Sticky particles” and Collisions

## Slide 3: Flocculation Overview
Channels
Upper Baffles
Ports between channels
Entrance
Lower Baffles
Exit

## Slide 4: Flocculation Overview
H = Water depth
L = Length of the flocculator channel
S = Space between baffles (and between the bottom of the tank and bottom of the upper baffles)
H
L
S
S
S
Upper baffle
Lower baffle
Minimum water level
Port from previous channel
Exit to the sedimentation tank entrance channel

## Slide 5: Collision Potential
Ability to Provide Collisions Between Flocs
Characteristic of the Flocculator
  Increase Size of Floc (to a point)
  Make it Easier for Flocs to Settle Out In Sed Tank
  Lower Residual Turbidity in Effluent

## Slide 6: Why Would We Recycle Flocs?
Collision Potential Required for Varying Influent Turbidities

## Slide 7: What is a Venturi?
Venturi In Action
Notes: -Reduction in fluid pressure from a contraction in pipe cross-sectional area
-Venturi effect is based upon the Bernoulli Equation
-Low Pressure created by the increased velocity creates a vacuum in the contraction

## Slide 8: How Would a Venturi Be Used in an AguaClara Plant?
Recycle flocs from the floc blanket in the Sedimentation Tank
Notes: Venturi must overcome head loss through plant (expansion of venturi, flocculator, sed tank is negligible and recycle pipe) – this determines how much head the vacuum needs to overcome

## Slide 9: What Have We Done?
Notes: Make assumptions about turbidities, and do mass balance to size Recycle pipe (3%) – can improve with others research
Linked dimensions into source code (thanks design team), program sizes recycle, contraction, angles based on plant flow rate
We plan to: improve based on new research, iterate the code to get a table of necessary constrictions for different flows, test construction techniques/performance of our geometry (smushed pipe)