## Slide 1: Floc Sed Optimization Team
Final Presentation
August 3rd, 2012
Mary John
Kaditya Naidu
Elizabeth Henderson

## Slide 2: Challenges
Run tests varying the following conditions: turbidity, flocculator length, alum dose, flow rate, capture velocity and rate of floc recycle flow
Collect and format data in Mathcad
Maintain floc blanket throughout experiments
Ultimate goal: best performance at lowest cost
Notes: -

## Slide 3: New Challenge
Test to failure
At what flocculator length and alum dose does a floc blanket stop forming?

## Slide 7: Problems Encountered
Cleaning out the flocculator
Flooding our working space
Calibrating the pump (old-fashioned way)
Nested codes on Mathcad (Slow in rendering results)

## Slide 8: Methods
Changed flocculator length
Varied alum doses (60mg/L, 35mg/L, 10mg/L) after one solids residence time
200 NTU influent water

## Slide 9
Chart: 200 NTU influent, 20m flocculator length
| 60 | 35 | 10
With floc blanket | 1.879 | 1.5 | 1
Without floc blanket | 1.082 | 0.75 | 0.45

## Slide 10
Chart: 200 NTU, 15m flocculator length
| 60 | 35 | 10
With floc blanket | 2.54 | 2.542 | 1.754
Without floc blanket | 1.616 | 1.5 | 1.2

## Slide 11
Chart: 200 NTU, 2m flocculator, with floc blanket
| 10 | 35 | 60
 | 1.3 | 2.3 | 2.689
No control run, short on time
Wanted to test system to failure
Assumed it would follow same trend as other two experiments

## Slide 12: Results
Floc blankets act as a filter
pC star is higher with floc blankets than without (see control)
Lower alum doses yield similar results as higher alum doses
Possible to reduce flocculator length and alum dose, thus reducing cost
Notes: -

## Slide 13: Floc Blanket Failure
Floc blanket formed at shortest flocculator length and lowest alum dose, 200 NTU water
Reduced turbidity 100 NTU
Floc blanket failure occurred between 10mg/L-35mg/L alum dose

## Slide 14
200 NTU, 10mg/L alum dose, 2m flocculator
Floc Blanket Formation

## Slide 15
Floc Blanket Formation
200 NTU, 10mg/L alum dose, 2m flocculator

## Slide 16
Floc Blanket forms then Falls Apart
100 NTU, 35mg/L alum dose, 2m flocculator

## Slide 17: Future Work
Continuing to change variables including flow rate, capture velocity and rate of floc recycle flow
Use this data to determine optimal performance at lowest cost
Continue to test for more specific failure point