## Slide 1
Continuing research on the development of a mathematical model to explain the physics of filtration
For more info: StaRS Filter Theory wiki
StaRS Filter Theory | Symposium Spring 2017
StaRS Filter Theory
Notes: Abstract:
Dynamic models of rapid sand filtration have proved elusive in describing for the diminishing pore space and increasing head loss in a filtration run. Empirical data from this study show that head loss increases linearly over time despite filter breakthrough. Dirty filter bed head loss data show that minor losses add to head loss over time. A new model for dynamic filtration is proposed, which models captured particles as embedded rings of flocs in the filter bed. Particle removal through filtration is described with an active filtration zone of empty pores filling up with particles. This zone moves for particles to attach.
Notes: Goal-introduction

## Slide 2
Two main goals for this semester
Validate Washer Model
Publish the paper
StaRS Filter Theory | Symposium Spring 2017
Notes: Mythri : Notes- This semester we have two main goals which we would be working towards- 1) Validate washer model 2) Publish the paper
Use ideas and data from fall 2016 team,
Organize and Publish the paper

## Slide 3
Creating a mathematical model for dirty bed is complex
Model for dirty bed
Active zone hypothesis
StaRS Filter Theory | Symposium Spring 2017
Notes: Mythri Notes: - There has been models explaining the clean bed-no models for dirty bed. As the flocs accumulate, -dirty bed
Research on dirty bed- insights into filter performance and failure time

## Slide 4: Constriction model represents the pores as empty chambers
Constrictions
Expansions
StaRS Filter Theory | Symposium Spring 2017
Notes: Mythri: Our model is based on the constricted tube model. Past literature also confirms that the constricted tube model is the best model We believe that filter is made up of long tubes which has a series of constrictions and chambers. Constrictions are, the spaces where the sand particles are the closest to one another and the chambers are the volumes of larger pore spaces between tangent sand particles. The space in this picture is the pore volume in one single capillary tube for the constriction model. This is the vertical section of the tube
Source:
A new model for Granular porous media- A.C .Payatakes

## Slide 5: Spherical packing forms constrictions and expansions
StaRS Filter Theory | Symposium Spring 2017
Notes: Mythri: This is a 3 D model of four sand particles –packing- Four constrictions and one expansion

## Slide 6: Streamline convergence theory validates the constriction model
StaRS Filter Theory | Symposium Spring 2017
Notes: Mythri: - Before we get into the model, It is important to know what happens when water flows through the model, water flows through constrictions-streamline converges
When water flows pass through the constrictions, streamlines diverge.

## Slide 7
A mass balance determined the volume of flocs in the filter
The volume of flocs is much less than the pore volume
StaRS Filter Theory | Symposium Spring 2017
Notes: ROSE: Our goal is to determine the dimensions of the floc buildup in the filter. The first thing we did to determine the geometry was to perform a mass balance on the filter by comparing influent and effluent turbidity. The mass of flocs left in the filter at failure is equal to the mass that entered throughout the test minus the mass that exited. Using an estimated floc density, the mass of flocs in the filter was converted to a volume.
The total volume of available pore space in the filter can be found using the porosity of the sand. Compared to this volume, the volume of flocs is very small.

## Slide 8
The floc buildup geometry must be very small
?
The proposed geometry is a washer
StaRS Filter Theory | Symposium Spring 2017
Notes: ROSE: Since very little mass actually accumulates in the filter, the volume of whatever geometry forms at the constrictions must be very small. The most intuitive geometry is a simple washer in which flocs accumulate around the edges of the constriction in a ring which builds inward and upward over time. The growth of the washer is limited by shear, since as the inner diameter of the washer contracts, the velocity of water moving through the washer increases.

## Slide 9
If washers are forming, minor losses should occur in a dirty bed
StaRS Filter Theory | Symposium Spring 2017
Notes: ROSE: The washer geometry would be expected to cause sudden flow expansions, leading to minor head loss in a dirty bed. If something similar to the washer geometry exists, we should see experimentally an appearance of minor losses in a dirty bed.

## Slide 10
Head loss in a clean bed is linear, since there are only major losses
StaRS Filter Theory | Symposium Spring 2017
Notes: ROSE: As a basis for comparison, in a clean bed the losses are only major, since when head loss is plotted versus velocity the plot is linear.

## Slide 11
In a dirty bed, head loss is nonlinear, indicating the presence of minor losses
StaRS Filter Theory | Symposium Spring 2017
Notes: ROSE: Comparing head loss to velocity in a dirty bed yields a nonlinear relationship, showing that there are minor losses occurring in a dirty bed. This supports the existence of a washer-like geometry.

## Slide 12
Inner diameter
of washer = D.Orifice
Minor loss component can be used to calculate washer dimensions
Diameter of
constriction = D.Pipe
StaRS Filter Theory | Symposium Spring 2017
Notes: The minor loss component can then be used to calculate the inner diameter of a washer. Currently, we are using the flow expansion formula to represent the flow contraction through a washer and its expansion into the expansion. However, we assume that there is no vena contracta due to gradual flow expansion in the expansion, so pi VC is 1. Our preliminary calculations suggest that the minor loss we measured in our dirty bed is actually smaller than what we would expect given the known diameter of the constriction. We are still working on figuring out what could be happening here.

## Slide 13
Increase in major loss can be used to calculate washer height
Height
of washer
P.In
P.Out
Shear
StaRS Filter Theory | Symposium Spring 2017
Notes: We can use the increase in major loss to calculate washer height. The underlying assumption here is that the flow accumulate additional shear as it passes through the washers. Therefore, we can use a force balance to determine the length through which the flow must pass to create the corresponding pressure drop. The challenge is that the washers are very small and we assume that the flow through the washer will not fully develop into a parabolic velocity profile. Hence, we are considering the flow through the washer to be similar to the flow over a flat plate. More analysis will need to be done here as well.

## Slide 14
Washer volume can be compared to volume of flocs retained in filter at failure
StaRS Filter Theory | Symposium Spring 2017
Notes: The dimensions of the washer can then be used to calculate a volume of accumulated flocs at each constriction. This value will be compared to experimental data previous teams collected to validate the washer model.

## Slide 15: Particles are removed in the active filter zone
Dirty Bed
Clean Bed
Active Zone
StaRS Filter Theory | Symposium Spring 2017
Notes: Lucinda
With a better understanding of what is happening microscopically at each constriction, we began to hypothesize about the macroscopic process in the filter. Here we will only look at a sand filter layer that has top-down flow and we will visualize the flocs entering from the top. Initially, the sand bed is entirely clean bed; no flocs have attached to the sand grains. As flocs stick to sand particles, washers being to form and the growing washers create the active zone. Therefore we can say that the active zone is where washers are developing. When washers have reached maximum volume, that region of the filter becomes part of the dirty bed.
Assume active zone is the same length (linear head loss, uniform particle attachment) and dirty and clean bed lengths are changing. Looking at effluent turbidity data, there is slight increase in performance throughout a filtration run and since the only parameters changing during a filtration run is the change in dirty and clean bed lengths, the data suggests that the increase in filter performance is due to the increased length of dirty bed and decreased length in clean bed.

## Slide 16: Head loss is linear until failure
Filter Failure
Time (hr)
Head Loss (cm)
StaRS Filter Theory | Symposium Spring 2017
Notes: The active zone Here is head loss data from a few experiments the spring 2016 team ran. The triangles represent filter failure and as the data suggests, head loss is linear until filter failure. This correlates with the active zone hypothesis in which regions of the filter

## Slide 17
There is a lot more work to be done
StaRS Filter Theory | Symposium Spring 2017
Notes: Looking at the goals we have for this semester, we realize that we have a lot of work to do. We are currently in the process of validating and finalizing the washer model, preparing the first draft of the paper, and while we say that literature review happens at the beginning of the semester, we will be reviewing literature throughout the semester. Hopefully by the end of this semester, we will submit the paper for the publication process.

## Slide 18
Questions
and
Recommendations
Mythri K
M Eng, Civil and Environmental Engineering
mk2446@cornell.edu
Lucinda Li
BS Environmental Engineering
li555@cornell.edu
Rose Linehan
BS Civil Engineering
rvl24@cornell.edu
StaRS Filter Theory | Symposium Spring 2017

## Slide 19
Appendix
Slides
StaRS Filter Theory | Symposium Spring 2017
Notes: From this point on, add any slides with figures that will help support your thesis. You might pull these figures from your Final Report.

## Slide 20: Filter Schematic
StaRS Filter Theory | Symposium Spring 2017

## Slide 21: Conditions used to test the filter
PACl Dosage (mg/L): 0.2, 0.65, 1.1, 1.55, 2
Influent Turbidity: 5 NTU
  Variable controlled by PID
Flow Rate: 118 mL/minute
Sand Size: Sieved at 30-35
Procedure
  Run Time: 12 hours
  Backwash
StaRS Filter Theory | Symposium Spring 2017
Notes: Procedure and experimental conditions
PID

## Slide 22: Filter performance is inconsistent
StaRS Filter Theory | Symposium Spring 2017
Notes: Influent turbidity at 5 NTU, flow rate at 0.98 mL/s, PACl dosage at 2 mg/L – same experiment over and over, but breakthrough/failure times are different for all of them – ranging from 1.5 hours to 3 hours
Two filter runs have similar failure times of 3 hours – but this result is inconsistent with failure times we expected with other coagulant dosages

## Slide 23: Clean Bed Head Loss
Chart: Head Loss over Time
StaRS Filter Theory | Symposium Spring 2017
Notes: Clean bed head loss over time during experiment
Each jump up shows an increase in flow rate, thus increasing head loss

## Slide 24: Dirty Bed Head Loss
Chart: Head Loss over Time
StaRS Filter Theory | Symposium Spring 2017
Notes: Dirty bed head loss over time during experiment
Each jump down shows a decrease in flow rate, decreasing head loss