## Slide 1: Arsenic Team
Tanapong Jiarathanakul, Imtiaz Karim, Michelle Wagner

## Slide 2: Outline
Goals
Accomplishment
  Experiment with Testing Procedures
Obstacles
  GFAAS
Future Plans
  Address this semester’s problems
  Begin testing with Arsenic

## Slide 3: Goals
Devise methods to conduct research safely
Determine the best way to prepare and measure very low concentrations of arsenic
Design a small scale reactor system
Prepare test groundwater

## Slide 4: What we have done so far
Preparation of lab space
Gathering of materials
Making groundwater solution
Practicing with dilution series and calibration curves
Experiment with testing procedures

## Slide 5
Standard Testing Procedure Experiment

## Slide 6: Goals
Design a standard reactor system using available lab equipment
Determine the ability for the tumbler and centrifuge to emulate flocculation, sedimentation and filtration

## Slide 7: Methods
Four types of testing procedure
  Regular centrifuge tube (sedimentation)
  Tube with filter basket (filtration)
  Tube with coated filter basket without coagulant dose (coated-media filtration)
  Tube with coated filter basket with coagulant dose (coated-media filtration)
Notes: Explain how you coat the filter

## Slide 8: Calibration Curve
Dilution series of 1, 2, 3, 4, 5 and 6 NTU
Notes: Note** 600 nm range

## Slide 9: Calibration Curve
Dilution series of 1, 2, 3, 4, 5 and 6 NTU

## Slide 10: Calibration Curve
Dilution series of 10, 20, 30, 40, and 50 NTU

## Slide 11: Calibration Curve
Chart: Turbidity Calibration Curve
| 0 | 10 | 10 | 20 | 20 | 30 | 30
 | -0.0001 | 0.0147 | 0.0183 | 0.0408 | 0.0393 | 0.0583 | 0.0617

## Slide 12: Sample Preparation
Turbidity = 5 NTU
PACl concentration = 2, 20 and 200 mg/L
Tumbler: Time = 5 minutes
Centrifuge: Time = 10 minutes, Power = 1

## Slide 13: Results
Chart: Turbidity Reduction Using Various Removal Methods
| 2 | 20 | 200
Sedimentation | 6.43 | 10.08 | 0.506
Filter | 7.15 | 7.78 | 10.9
Coated Filter | 2.57 | 1.45 | 1.54
Coated Filter with Coag Dose | 1.96 | 3.27 | 0.67
Notes: Spectrometer requires at least 0.6 mL of sample
Transfer of solution may cause resuspension

## Slide 14: Results
Chart: Turbidity Reduction using Sedimentation and Filtration
| 2 | 20 | 200
Sedimentation 1 | 1.5 | 0.7 | 3.25
Sedimentation 2 | 0.65 | 5 | 1.55
Filtration 1 | 0 | 0 | 0
Filtration 2 | 0 | 0 | 0
Notes: Sedimentation is not a reliable method

## Slide 15: Conclusion
Sedimentation is not a reliable method
Filtration and coated filtration successfully removed turbidity
We will have to rerun this experiment with arsenic
We also need to adjust the time and power for the tumbler and centrifuge

## Slide 16
Obstacles

## Slide 17: GFAAS Issues
Changing the type of matrix modifier we are using
Replace old tubing

## Slide 18: pH Problems
We did not considered the effect of pH in our samples
  PACL has low pH
  Groundwater solution has pH of 7.98
Notes: Mention ideal pH = 7 for PACl to work properly

## Slide 19: Testing Procedures
Problems with coating filter basket
Chart: Turbidity Removed using Coated Filtration with and without Coagulant Dose
| 2 | 20 | 200
Coated Filter 1 | 2.45 | 2 | 4.85
Coated Filter 2 | 0 | 0 | 2.2
Coated Filter with PACl Dose 1 | 0 | 4.3 | 64.55
Coated Filter with PACl Dose 2 | 40.15 | 4.05 | 20.55

## Slide 20
Future Works

## Slide 21: Future Works
Use GFAAS to test Arsenic
Test for different factors:
  Type of coagulant
  Oxidation state
  Clay or not clay/turbidity
  pH

## Slide 22: GFAAS
Align the sample platform with the light beam
Adjust the sampling arm
Create calibration curve

## Slide 23: Experiment with Arsenic
Test the effects of these factors on arsenic removal
  Types of coagulant
  Oxidation state
  Turbidity
  pH

## Slide 24: Questions?

## Slide 25: Acknowledgements
Thank you:
Professor Lion
Professor Weber-Shirk,
William Pennock
Casey Garland
Working harder to keep arsenic out of your water!