## Slide 1: Wastewater Treatment
Ge Gao, Maithili Gokarn, Walker Grimshaw, Ethan Keller, Caitlin McKinley, Amiel Middelmann, Luke Zhu
Notes: walker

## Slide 2
Whole System
Anaerobic Treatment
  high strength wastewater
  energy neutral
  methane production -can run whole treatment plant or components of aerobic treatment plant
Aerobic Treatment
  higher efficiency
  nutrient removal
  more experience
Notes: walker

## Slide 3: Anaerobic Treatment

## Slide 4: UASB Reactors (Upflow Anaerobic Sludge Blanket )
Spring 2014
Gas tightness
Inoculation ~ 566 ml of bio-granules
Operation Changes:
• Double HRT
•Reduce pump flow rate to half
•Double strength of wastewater
heating
Data analysis
Notes: Vicky

## Slide 5
Biogas Production
COD Removal in the form of CH4 and CO2 gas production
Notes: Vicky

## Slide 6
Biogas Production
Notes: Vicky

## Slide 7
Average Daily Biogas Production
Biogas Production
Notes: Vicky

## Slide 8
Biogas Fate

## Slide 9
Biogas Fate
Captured and Volume Inferred With Pressure Reading
Through Solenoid
Transfer Over Gas-Liquid Interface at Weir
Bubbles go out Weir
Dissolved In Effluent
Through Cracks and Threads

## Slide 10
Biogas Collection Solutions
Increase WW Strength
Redundant Gas Collection (Wet Test Meter, Bubble Meter, Bag test)
Additional Collection
Cautious Construction
Raising Temperature
Ritter Bubble Meter
Wet Test Meter

## Slide 11
Correcting for gas losses from valve opening
Notes: Ethan

## Slide 12: 2.4: ~1090 ml biogas per day 2.5: ~1150 ml biogas per day
‘Bag’ Test
Notes: Caitlin

## Slide 13: Methane Gas Production
Calculate partial pressure of methane from standard curve equation .
Notes: Maithili

## Slide 14: Methane Gas Production UASB Reactor 2.4
Gas tight from April 12, 2014 to date
Producing methane gas - negative trend, more steep, than Fall 2013
Partial pressure lower than last semester.
Methane lost in effluent?
Notes: Maithili

## Slide 15
Methane Gas Production
UASB Reactor 2.5
Gas tight past 2 weeks
Producing small amounts of methane
Insufficient data to make conclusion
Notes: Maithili

## Slide 16: Average Daily Methane Gas Production
 | Fall 2013 Reactor 2.4 | Fall 2013 Reactor 2.6 | Spring 2014 Reactor 2.4
Average Daily Methane Production(ml) | 116.82 | 139.477 | 176.623
Methane Gas Production
Notes: Maithili

## Slide 17
Chemical Oxygen Demand

## Slide 18
% COD Removal

## Slide 19: Overall: 2.4 : 68.8% 2.5 : 77.7%
% COD Removal
2.5 before heating:
77.9 %
2.5 after heating:
77.6%
Heating Begins

## Slide 20: Reactor Modifications - Heating

## Slide 21: Microbial Growth Rate and Temperature

## Slide 22: Parameters
Tube L = 19 ft
Tube D = 0.5 in
Number of coils = 22
Bath Temp = 55°C
Reactor Temp = 32°C

## Slide 23: Heating start-up
Two hours to reach steady temperature

## Slide 24: Temperature Profile

## Slide 25: Large Reactor
Solution:
  Substrate change?
  Larger Reactor?
  Also optimize
    Methane Collection
    Gas Tightness
    Versatility
  Temperature Change
    Heated Room

## Slide 26: Anaerobic Conclusions
Current Gas Measurement method is insufficient and inaccurate
Heating the reactors has not yet caused improvement in COD removal and gas production

## Slide 27: Future Directions
Temp and COD removal/gas production relationships
Vary influent strength
Gas meter
Energy balance for production and use

## Slide 28: Aerobic Treatment

## Slide 29: From anaerobic to aerobic

## Slide 30: Still focusing on granules
5 cm
2 - 5 mm

## Slide 31: Granule Sequencing Batch Reactor (GSBR)
Operation States

## Slide 32: Granule Sequencing Batch Reactor (GSBR)
Advantages
- Biomass retention
- No settling tank
- Simultaneous nitrification/ denitrification
Disadvantages
- Aeration requirement
- Difficult to cultivate granules
- Sequenced batch considerations

## Slide 33: Simultaneous Nitrification and Denitrification (SND)
High nitrogen removal at 20% O2 saturation (de Kreuk et. al.)
Dependent upon presence of storage polymers
Aerobic
Anaerobic

## Slide 34: PAOs and GAOs
Acetate converted into storage polymers (PHB) in anaerobic stage
Phosphate taken up during aerobic stage to make poly-phosphates

## Slide 35: Reactor Operation

## Slide 36: Determining aeration rate

## Slide 37: Determining aeration rate

## Slide 38: Aeration - transfer efficiency
Flow Rate (uM air/s) | Flow Rate (g 02/day) | Oxygen Transfer Rate (mg/L-day) | OLR (mg/L-day) | O2 Transfer Efficiency
100 | 58 | 3700 | 2500 | 3.5%
500 | 290 | 5900 |  | 1.1%
1000 | 580 | 9300 |  | 0.88%
2000 | 1160 | 9400 |  | 0.45%

## Slide 39: Dissolved Oxygen Issues

## Slide 42: Aeration
Issues with monitoring DO

## Slide 43: COD Removal
Average Influent Concentration: 1180.33 mg/L St Dev: 158.75 mg/L
 | COD Removal w/o Particulate | COD Removal w/ Particulate
4/28 | 82% | 26%

## Slide 44: No Granules and Reactor Clogging
Flocculant growth prevented mixing
- insufficient mixing from baffle
- new design!

## Slide 45: Larger Reactor
No baffle in current design - Bubble Column
Airlift reactor offers high shear zones which
increase granule stability
Bubble Column easier to implement
- longer startup time before granulation
Increase anaerobic time
- Increases granule stability, phosphate removal, simultaneous nitrification/denitrification (SND)
- 60 min anaerobic feed, aerobic period with O2 saturation of 20%

## Slide 46: Large Reactor D.O.
Begin Aeration

## Slide 47: Aerobic Conclusions
Granule cultivation is difficult
Reactor operation set up relatively easily
Insufficient mixing leads to flocculation, settling and clogging
Biomass growth on walls and aeration stones is excessive. Must be removed

## Slide 48: Future Directions for Aerobic Treatment (this summer)
Implement anaerobic idle time
Characterize granules
    size, density (SVI)
    locate PAOs (DAPI stain)
Monitor N, P removal
Change influent composition to better mimic wastewater
Construct more reactors to compare operation changes