## Slide 1: Introduction to Teams

## Slide 2: Potential Teams
Chemical Dose Controller
Ram Pump
Laminar Tube Flocculator
Turbulent Tube Flocculator
Floc Probe
Enclosed Stacked Rapid Sand Filter
Stacked Rapid Sand Filter Backwash
Foam Filtration
Village Supply System
Small Scale Plant Model
Water Treatment Technology Selection Guide
Design
Public Relations

## Slide 3: CDC (Chemical Dose Controller)
The CDC couples the plant flow rate with the flow rate of the coagulant
Objectives:
  Assemble CDC from current guidelines.
  Assemble and test dosers designed for different flow rates

## Slide 4: CDC (Chemical Dose Controller)
  Test units at stock concentrations used in AguaClara facilities
  Develop a set of dosers that can be shipped where needed
  Skills: Fabrication, fluids, physics

## Slide 5: Ram Pump
There is an old technology that used hydraulic transients to lift water from a stream to a higher elevation. The device was called a “Ram Pump”and it made a rhythmic clacking noise.
High pressure pipe
Stream
Ram Pump
Source pipe

## Slide 6: Ram pump
Objectives:
  Maintain contact with AguaClara team in Honduras to resolve issues in the field
  Design and build an effective recycling system that will make it easy to conduct extensive tests and operate without human intervention.
  Conduct extensive testing to measure reliability and efficiency.
Skills: Fabrication, fluids, physics

## Slide 7: Laminar Tube Flocculator
Objectives:
  Repeat experimentation to obtain consistent results.
  Explore floc break up and tapered flocculation
  Explore alternate flocculator designs to enhance performance

## Slide 8: Turbulent Tube Floc
Objectives:
  Build adjustable effluent elevation to achieve target flow rates.
  Remove air from effluent of flocculator.
  Design for 12 hour tests without replacing the PACl stock, and use a target range of PACl doses.

## Slide 9: Floc Probe
Objectives: develop an easy method for operators to monitor floc blanket depth and the depth of sludge in the floc hopper
Potential options:
  Eye as detector
    Sludge judge (transparent tube with valve at bottom that can grab a column of water from within the sed tank)
    Submersible LED light
  Sensors (ultrasound, optical)
Preferable skills: fabrication of detectors, experimentation to measure ease of use

## Slide 10: EStaRS – Enclosed Stacked Rapid Sand Filters
Objectives:
Design a filter test system that facilitates extended hydraulic and turbidity testing.
Keep in touch with AguaClara team in India to resolve technical issues
Design Improvements:
Skills: Fluids, Fabrication

## Slide 11: Stacked Rapid Sand Filter Backwash
Objectives:
  Develop rational guidelines for the selection of sand for Stacked Rapid Sand Filters
  Develop an experimental apparatus that will allow measurement of sand size distribution in a fluidized sand bed
  Select the optimal expansion ratio for cleaning
  Skills: Fluids, fabrication,

## Slide 12: Foam Filtration
Objective: design and test a neatly packaged and portable filter
Design LFOM to be integrated
with the float valve for dose controller.
Make lever system more compact.
Test foam filter through cycles of filtration and cleaning.
Preferable skills: fabrication, design, fluids

## Slide 13: Small Scale Plant Model
Objective: Produce an updated scale model of AguaClara technologies that is easy to transport in carry on luggage.
Impact: use for teaching about AguaClara technology at Cornell, PR, and conferences
Skills: Fabrication, problem solving
Note: CEE 2550 Only

## Slide 14: Water Treatment Technology Selection Guide (WTTSG)
Objective: develop a guide to indicate the constraints that determine which technology is best suited for different levels and types of contamination
Must be designed as a front end for the AguaClara design engine
Skills: Drinking water treatment, website creation online forms

## Slide 15: Village Supply System
Objective: Design distributed storage for a village water supply
Evaluate designs that eliminate the need for an elevated storage tank and an elevated AguaClara plant

## Slide 16: Village Supply System
Design of the photovoltaic and pump system
Design of the distribution system (pipe sizes), pressure target, and flow restrictions
Design of household safe water infrastructure
Skills: Water treatment, photovoltaics, pumps, Mathcad

## Slide 17: Design Tool
Mathcad
Design
Mathcad
Drawing Code
User Inputs
LabVIEW
Design Engine
Plant
Design
AutoCAD
MS Word

## Slide 18: Design Tasks
  Incorporating new research progress into the design
  Designing plants for a greater range of flow rates
  Making our designs more easily understood
  Communicating with the teams in Honduras and India, and with new implementation partners, to address concerns

## Slide 19: The Drawing

## Slide 20: Public Relations
Objectives:
Manage all AC media forms and increase our activity/likes/tweets/connections etc.
Unit processes videos including AguaClara plant walk through
AguaClara Apparel!
Research and network with other NGO’s that could be potential implementation partners
Note: CEE 2550 Only

## Slide 21: Expectations
All team members are expected to:
  Spend at least 10 hours per week working on their project (including time in class)
  Consistently meet with subteam
    Be respectful of teammates & show up to meetings on time
  Always attend full class meetings
  Submit reports on time
  Clean up after themselves in the lab

## Slide 22: Interviews
Sign up on the sheet or online
Held in Hollister B60
  We can show you where this is after class if you ask
Will last approximately 15 minutes
Will determine admission onto the overall team as well as team placement

## Slide 23: Pre-Interview Tasks
Review How Water Flows Through the Plant
  This will help you understand the challenges
Read the Team Challenges page
Fill out the team organization survey

## Slide 24: Next Steps
https://confluence.cornell.edu/display/AGUACLARA/Syllabi