## Slide 1: High Rate Sedimentation Plate Settlers
Aobei Cheng
Sidney Lok
Yuqi Yu
Lishan Zhu
Notes: Sidney

## Slide 2: Introduction
Affordability more communities
Large plants cost more…
  space
  money
Notes: Sidney

## Slide 3: Introduction
Smaller sedimentation tank
higher upflow velocity
flocs go out of tank
Focus: concentrating the floc blanket
Notes: Sidney

## Slide 4: Goals for the semester
Maintain a colloidal particle blanket at upflow velocities higher than 1 mm/s
Explore different plate settler geometries to concentrate floc density
Notes: Sidney

## Slide 5: Flocculator Design
Notes: Yuqi

## Slide 6: Flocculator Design
Flocculator tubing diameter:
0.95 cm (⅜ inch)
Flow Rate (Q):
Energy Dissipation Rate (ε):
ε=4057mW/kg
ε should be between 5 and 10 mW/kg!
Notes: Yuqi

## Slide 7: Flocculator Design
Keep using the ⅜ inch flocculator in addition to the energy dissipation rate constraints to return the flow rate.
When Q=7mL/s, ε=6.963mW/kg
Notes: Yuqi

## Slide 8: Flocculator Design Take II
Increase of tubing from ⅜ inch to ⅞ inch diameter
Settling of “monster flocs” on tube walls
Modified the flocculator shape
Notes: Albert

## Slide 9: Flocculator Design Take III
Notes: Albert

## Slide 10: Flocculator Design Take III
Figure eight design = more circulation at bends of flocculator
Circulation should continuously push the flocs through the tube
We ran the apparatus but...
Notes: Albert

## Slide 11: Flocculator Design Take III
Air pockets at the top bends of flocculator are preventing flow
Air pockets
Notes: Albert

## Slide 12: Flocculator Design Take III
Ran water vertically to remove air bubbles
Use 80/20 to fix pipes on lab bench
Notes: Lishan

## Slide 13: Future work
Remove air pockets and run the modified tube flocculator apparatus
Design and create our sedimentation tank
Start experiments with plate settlers in our full apparatus:
  Continuous plates
  Porous plates
  Zigzag plates
  Combinations
Notes: Lishan

## Slide 14: Questions?
Thanks for listening!