## Slide 1: Una herramienta de diseño automático (ADT) para plantas potabilizadoras sostenibles de energía gravitacional
Autores:
  Monroe L. Weber-Shirk
  Leonard W. Lion
  Maysoon Sharif
  Jeffrey C. Will
Notes: Click on the picture of the plant to design a plant

## Slide 2: Contenidos
¿Quién somos?
La razón por que tecnologías convencionales fracasan
Nuestra filosofía de diseño
La ADT
Nuestra manera de innovación
La prueba

## Slide 3: ¿Quién somos?
Con apoyo de:
Notes: AguaClara at Cornell is a group of students and faculty who conduct research and provide hydraulic designs for gravity-powered (electricity-free) water treatment plants

## Slide 4: Un resumen visual
Ladrillos hecho en la comunidad
Ingeniero hondureño
Maestro de obra hondureño
Ayudantes de la comunidad
Construcción de la planta de Atima, Sta. Bárbara, Honduras
Albañil hondureño
Técnico hondureño
Notes: AguaClara includes the engineers, specialists, and community members that conduct the outreach and manage involvement to ensure that plants operate successfully in the long-term

## Slide 5: Nuestra red
Cornell University
AguaClara R&D
Apoyo de innovación
Apoyo técnico de implementación
Apoyo de diseño y implementación
Guatemala AP INFOM
Nicaragua AP CARE
AguaClara Inc.
Ethiopia AP Bahir Dar U
Colombia AP AguaNova
Cada socio va a crear su propia red de comunidades con plantas AguaClara
Universidad
Empresa privada
Ministerio gubernamental
ONG Internacional
Implementation
& Innovation
Partner (APP)
Notes: AguaClara Inc. Si a collaborative partner with implementers, not competitive, offering technical support, design review, and implementation support

## Slide 6: Contenidos
¿Quién somos?
La razón por que tecnologías convencionales fracasan
Nuestra filosofía de diseño
La ADT
Nuestra manera de innovación
La prueba

## Slide 7: Retos alcanzados por AguaClara
Reactores cerrados
Partes de alta especialización
Falta de apoyo técnico
Falta de mano de obra calificado
Operación difícil

## Slide 8: ¿Porqué fracasa la tecnología convencional?
El diseño no está basado en la física fundamental
Notes: Most advances in water treatment technology in the last fifty years have focused on automation, rather than innovation or optimization of the treatment processes themselves. You end up with complicated control boards that people don’t know how to use. This is the actual control board at Siguatepeque. When we asked the operator how to read the control board, he said he had no idea and that they don’t use it.

## Slide 9: Teconolgías inapropiadas
Filtros rápidos de arena abandonados en la Ciudad de Guatemala
Válvulas de control numáticas en Santa Rosa de Copán
Notes: Pressurized filters – closed so you can’t see inside. Can’t even be sure if sand is still in there. Complicated piping – it’s hard to tell what some valves are used for. Valves break easily, are expensive, and hard to replace. In Honduras they need to custom make valves to replace them.

## Slide 10: Contenidos
¿Quién somos?
La razón por que tecnologías convencionales fracasan
Nuestra filosofía de diseño
La ADT
Nuestra manera de innovación
La prueba

## Slide 11: Fílosofia de diseño
Reactores están abiertos
Todas partes están localmente disponible y no son caras
Fácilmente operable
No utilizan engería eléctrica
Notes: The first four points are just mentioning that AguaClara does not make the mistakes that lead to abandonment. Mention that AguaClara plants can be operated by someone with a 6th grade education under “easy to operate.”

## Slide 12: Alcanzando el reto
Notes: A look at the entrance tank to see how we do things differently. Brief overview of how water flows through/particles settle in the hoppers. Instead of expensive valves to drain each hopper, use a removable stopper. Hoppers make it easy to clean, because all of the sludge settles at the base of the drain. Linear flow orifice meter that makes it easy to read flow rate through the tank.

## Slide 13
Trash Rack
Overflow Weir
Chemical Dose Controller
LFOM
Hopper
Primary Sludge Drain

## Slide 14: La Planta
Alauca, El Paraíso
Marcala, La Paz

## Slide 15: Fílosofia de diseño
Algoritmos están basado en la física fundamental
Éxito y mejoramiento viene de las relaciones de largo plazo de las comunidades servidas
Notes: Now focusing on last two points.

## Slide 16: De la física
Tubo de mezcla rápida
Notes: We specifically depart from empirical design values in the algorithms for rapid mix, flocculation, and flow transitions into the sedimentation tank. The design of these pieces is conventionally based on the turbulent energy dissipation rate rather than the velocity gradient method (Weber-Shirk and Lion, 2010) because the velocity gradient method only applies to laminar flow reactors (Cleasby 1984).

## Slide 17: De la investigación
Notes: Basing algorithms on physics means challenging the basis of conventional design parameters. Plate settler spacing research – determining spacing as a balance between decreasing tank size and preventing floc rollup. Convention says 5cm, but our research suggests 2.5 which we currently use in our designs. The upper picture uses 2.5cm spacing, saving more than 30cm in depth as compared to the conventional spacing shown below.

## Slide 18: De los usuarios
Caja de entrada del filtro (de los tanques de sedimentación)
Caja de Salida
Notes: Mention lessons learned and improvement and innovation cycle

## Slide 19: Contenidos
¿Quién somos?
La razón por que tecnologías convencionales fracasan
Nuestra filosofía de diseño
La ADT
Nuestra manera de innovación
La prueba

## Slide 20: ¿Qué es la ADT?
Calculaciones de Mathcad
Archivos de dibujo de Mathcad
LabVIEW
AutoCAD
MS Word
Ingresos del usuario
Diseño de la planta

## Slide 21: ¿Qué es la ADT?

## Slide 22: El Diseño
Notes: Sample AutoCAD output from a design request.
Because of our approach, we have plants that are as old as 7 years. Conventional plants are often abandoned in 2 years.
The ADT combines the knowledge generated at Cornell and communities currently served by AguaClara plants to create robust, scalable designs that are appropriate for the social, environmental, and financial context of the regions they serve.

## Slide 23: Diseños Sostenibles
Ojojona, 2007
Cuatro Comunidades,
2009
Algalteca, 2010
Támara, 2008/2012
Marcala, 2008/2011
Aluaca, 2012
Notes: NOT JUST ENVIRONMENTALLY!
6 Fully-operation plants in Honduras, operated and maintained independently by the community
Community members have independently voted to increase their water tariffs, and water boards now have extra savings.
Water Boards are increasing their savings for emergencies and upgrades. Some using savings for sanitation like latrines and sewers

## Slide 24: Causa y efecto
Miembros de la comunidad ya no compran agua embotellada
Todas las plants cumple con la norma hondureña y el filtro cumple con la recomendción de la OMS
Centros de salud notan los efectos positivos
Hay menos niños con diarrea
Notes: Community members save money on bottled water. Before AguaClara plants, health centers did not keep a record of diarrhea cases because the numbers were so high. After AguaClara plants the number has decreased significantly, and they now keep record.

## Slide 25: Contenidos
¿Quién somos?
La razón por que tecnologías convencionales fracasan
Nuestra filosofía de diseño
La ADT
Nuestra manera de innovación
La prueba

## Slide 26: El ciclo de innovación
Análisis matemática
Investigaciones del laboratorio
Diseño automatico
Implementación de gran escala, capacitación, y transferencia de conocimiento
Evaluación
Notes: Incorporating feedback from the field ensures that ease of use is accounted for in designs. Two-way relationship of technical support to ensure plant longevity and feedback to improve designs.

## Slide 27: Innovaciones
Monte de lodos
Filtración rápida de arena en múltiples capas (FRAMCa)
Reciclación de floculos
Notes: The first bolded point – basing algorithms on fundamental physics gives us an edge in terms of innovation. We built the designed and built a one-of-a-kind stacked rapid sand filter, which incredibly successful. We are also beginning to understand how to create floc blankets, which will allow us to decrease the size of our sedimentation tanks. Also we are conducting research on floc recycle: returning sedimentation sludge to the start of the flocculator, to increase flocculation efficiency and therefore hopefully reduce the size of our flocculators.

## Slide 28: Tecnología innovadora
En lugar de brindar maquinería
AguaClara brinda conocimiento
En lugar de patentar la tecnología
AguaClara comparte el conocimiento y mejora rendimiento
Dieñamos para el contexto y usamos la experiencia del campo para mejorar

## Slide 29: Ahorramiento de costos
No toma en cuenta que plantas mecanizadas tiene una vida útil más corto ni el costo de
reparciones con partes patentadas
Chart: USD per 1 million liters
| Mechanized | AguaClara
chlorine | 7.5556 | 7.5556
coagulant | 18.16 | 18.16
electricity | 17.7778 | 0
capital | 30.4212 | 15.2106
finance | 23.5403 | 11.7701
Asumiendo cada planta tiene una vida útil de 25 años y ningún parte fracasa!
El costo de energía eléctrica es $0.16/kWhr, usando costos de químicos en Honduras en 2012
Notes: Current capital cost (15 – 20 USD per person served) is about a third of that of conventional plants of comparable size, and future innovations will make our capital costs even more competitive
Operation and maintenance costs (2 – 4 USD per person per year) are low enough that community members have volunteered to pay more
Cap cost = 4,000 – 8,000 USD/L/s

## Slide 30: Diseños probados
Notes: In the future, there will be already proofed hydraulic designs that can be downloaded freely, without the need to wait for a new design.
6,9,12,15,20,25,30, 40,....90
The image links to the design server site.

## Slide 31: Contenidos
¿Quién somos?
La razón por que tecnologías convencionales fracasan
Nuestra filosofía de diseño
La ADT
Nuestra manera de innovación
La prueba

## Slide 32: ¡Funciona!
Marcala, La Paz
Támara, Francisco Morazán

## Slide 33: El rendimiento
Chart: Fecha de 2011
Resultados de Cuatro Comunidades – Septiembre 2011
Fuente: datos del operador
Norma Hondureña y Brasileña

## Slide 34: ¡Gracias!
http://aguaclara. cornell.edu
www.apphonduras.org
www.cee.cornell.edu
Contacto:
Jeff Will
jcw57@cornell.edu